## Slide 1
Component Identification: Analog
Introduction to Resistors and Capacitors
© 2014 Project Lead The Way, Inc.
Digital Electronics

## Slide 2: Component Identification
This presentation will…
Introduce common components used in electronics.
Define a resistor and present various resistor types and package styles.
Demonstrate how to read a resistor’s nominal value and how to measure its actual value with a Digital Multi-Meter (DMM).
Define a capacitor and present various capacitor types and package styles.
Demonstrate how to read a capacitor’s nominal value.

## Slide 3: Resistors
A resistor is an electronic component that resists the flow of electrical current.
A resistor is typically used to control the amount of current that is flowing in a circuit.
Resistance is measured in units of ohms () and named after George Ohm, whose law (Ohm’s Law) defines the fundamental relationship between voltage, current, and resistance.

## Slide 4: Resistors: Types and Package Styles
Surface Mount Resistors
Variable Resistors
(potentiometer)
Carbon Film Resistors
5 Bands
Carbon Film Resistors
4 Bands

## Slide 5: Resistors: Size Comparison

## Slide 6: Determining A Resistor’s Value
Color Code
Resistors are labeled with color bands that specify the resistor’s nominal value.
The nominal value is the resistor’s face value.
Measured Value
A Digital Multimeter DMM can be used to measure the resistor’s actual resistance value.

## Slide 7: How To Read A Resistor’s Value
Resistor Color Code

## Slide 8: Resistor Value: Example #1
Example:
  Determine the nominal value for the resistor shown.
1
0
X 100
1000 Ω
1 kΩ

## Slide 9: Resistor Value: Example #2
Example:
  Determine the nominal value for the resistor shown.
3
X 100K
3000 kΩ
3 MΩ
0

## Slide 10: Resistor Value: Example #3
Example:
  Determine the color bands for a 1.5 K  5% resistor.
?
?
?
?
Brown
Red
Green
?
?
?
?

## Slide 11: Measured Value
Using a Digital Multi-Meter (DMM) to measure resistance.

## Slide 12: Capacitors
A capacitor is an electronic component that can be used to store an electrical charge.
Capacitors are often used in electronic circuits as temporary energy-storage devices.
Capacitance is measured in units of farads (F) and named after Michael Faraday, a British chemist and physicist who contributed significantly to the study of electromagnetism.

## Slide 13: Capacitors: Types and Package Styles
Electrolytic Capacitors
Mylar / Tantalum
Monolithic Ceramic
Electrolytic Capacitors
Ceramic Disc Capacitors
Radial Lead
Axial Lead

## Slide 14: Capacitors: Types and Package Styles
Size Comparison
Surface Mount
Ceramic Capacitors
Surface Mount
Tantalum Capacitors

## Slide 15: How To Read A Capacitor’s Value
Electrolytic Capacitors
10 F +-20%
0.47 F+-20%

## Slide 16: How To Read A Capacitor’s Value
4
First Digit
First Figure
Second Digit
Second Figure
Third Digit
# of Zeros
Fourth Digit
Tolerance
7
2
K
4
7
00
K
4700 pF 10%
Code | Tolerance
A | ±0.05%
B | ±0.1%
C | ±0.25%
D | ±0.5%
F | ±1%
G | ±2%
J | ±5%
K | ±10%
M or NONE | ±20%
N | ±30%
Q | −10%, +30%
S | −20%, +50%
T | −10%, +50%
Z | −20%, +80%
Disc Capacitors
Note: Units on Disc Capacitors are always in pico-farads

## Slide 17: Capacitor: Example #1
Example:
  Determine the nominal value for the capacitor shown.
Code | Tolerance
A | ±0.05%
B | ±0.1%
C | ±0.25%
D | ±0.5%
F | ±1%
G | ±2%
J | ±5%
K | ±10%
M or NONE | ±20%
N | ±30%
Q | −10%, +30%
S | −20%, +50%
T | −10%, +50%
Z | −20%, +80%
3
0
±5%
3
330 pF ±5%

## Slide 18: Capacitor: Example #2
Example:
  Determine the nominal value for the capacitor shown.
Code | Tolerance
A | ±0.05%
B | ±0.1%
C | ±0.25%
D | ±0.5%
F | ±1%
G | ±2%
J | ±5%
K | ±10%
M or NONE | ±20%
N | ±30%
Q | −10%, +30%
S | −20%, +50%
T | −10%, +50%
Z | −20%, +80%
1
000
±10%
0
10000 pF ±10%

## Slide 19: Common Electronic Components Displays
Seven Segment Display
Light Emitting Diodes (LED)
1
2

## Slide 20: Common Electronic Components Miscellaneous Components
1
2
3
Fuses
Diodes
Voltage Regulator