## Slide 1
Analog and Digital Signals
Digital Electronics

## Slide 2: Analog & Digital Signals
This presentation will
Review the definitions of analog and digital signals.
Detail the components of an analog signal.
Define logic levels.
Detail the components of a digital signal.
Review the function of the virtual oscilloscope.
Notes: Introductory Slide / Overview of Presentation

## Slide 3: Analog and Digital Signals
Analog Signals
Continuous
Infinite range of values
More exact values, but more difficult to work with
Digital Signals
Discrete
Finite range of values (2)
Not as exact as analog, but easier to work with
Example:
A digital thermostat in a room displays a temperature of 72. An analog thermometer measures the room temperature at 72.482. The analog value is continuous and more accurate, but the digital value is more than adequate for the application and significantly easier to process electronically.
Notes: This slide defines analog and digital signals and gives several examples of each.

## Slide 4: Example of Analog Signals
An analog signal can be any time-varying signal.
Minimum and maximum values can be either positive or negative.
They can be periodic (repeating) or non-periodic.
Sine waves and square waves are two common analog signals.
Note that this square wave is not a digital signal because its minimum value is negative.
0 volts
Sine Wave
Square Wave
(not digital)
Random-Periodic
Notes: Examples of common analog signals.

## Slide 5: Parts of an Analog Signal
Amplitude
(peak-to-peak)
Amplitude
(peak)
Period
(T)
Frequency:
Notes: Parts of an analog signal: amplitude, period, & frequency.

## Slide 6: Logic Levels
Before examining digital signals, we must define logic levels. A logic level is a voltage level that represents a defined digital state.
Logic HIGH: The higher of two voltages, typically 5 volts
Logic LOW: The lower of two voltages, typically 0 volts
5.0 v
2.0 v
0.8 v
0.0 v
Logic Low
Logic High
Invalid
Logic
Level
Logic Level | Voltage | True/False | On/Off | 0/1
HIGH | 5 volts | True | On | 1
LOW | 0 volts | False | Off | 0
Notes: This slide introduces the concept of logic levels for , gives the range of acceptable voltages for a logic high & low related to LS TTL, and lists other common terms used to describe logic levels.

## Slide 7: Example of Digital Signals
Digital signal are commonly referred to as square waves or clock signals.
Their minimum value must be 0 volts, and their maximum value must be 5 volts.
They can be periodic (repeating) or non-periodic.
The time the signal is high (tH) can vary anywhere from 1% of the period to 99% of the period.
0 volts
5 volts
Notes: Examples of common digital signals.

## Slide 8: Parts of a Digital Signal
Amplitude
Time
High
(tH)
Time
Low
(tL)
Period (T)
Rising Edge
Falling Edge
Amplitude:
  For digital signals, this will ALWAYS be 5 volts.
Period (T):
  The time it takes for a periodic signal to repeat. (in seconds)
Frequency (ƒ):
  A measure of the number of cycles of the signal per second. (in Hertz, Hz)
Time High (tH):
  The time (in sec.) the signal is high or 5v.
Time Low (tL):
  The time (sec.) the signal is low or 0v.
Duty Cycle (DC) (%):
  The ratio of tH to the period (T), expressed as a percentage.
  Rising Edge:
  A 0-to-1 transition of the signal.
Falling Edge:
  A 1-to-0 transition of the signal.
Frequency (ƒ):
Duty Cycle (%):
Notes: The parts of a digital signal: amplitude, period & frequency, time high, time low, duty cycle, rising & falling edge.

## Slide 9: Oscilloscope
The oscilloscope is a piece of electronic test equipment that is used to capture and measure time-varying signals, both analog and digital.
Oscilloscopes
  can be found on the workbench (physical)
  as part of a simulation tool (virtual)
  as part of virtual instrumentation package on your computer (software)
We will limit our usage to the virtual oscilloscope initially until we are ready to measure actual circuits.

## Slide 10: Virtual Oscilloscope: Multisim
4 Channel Oscilloscope
Component
X axis plots time
Timebase Scale & X Position:
  Adjusts the time scale and offset of the signals. This is common for all channels.
Channel Scale & Y Position
  Adjusts the horizontal scale and offset of the selected channel.
Channel Selector
Marker Display:
  Displays the voltage & time intersect for the markers T1 & T2.
Markers:
  Movable markers T1 & T2
Displayed Signals
Y axis
plots
voltage
Notes: Review with the student Multisim Oscilloscope.

## Slide 11: Example: Digital Signal
Example:
  Determine the following information for the digital signal shown:
  Amplitude
  Period (T)
  Frequency (ƒ)
  Time High (tH)
  Time Low (tL)
  Duty Cycle (DC)
Notes: Pause the presentation and allow the student to work on the example. The solution is on the next two slides.

## Slide 12: Example: Digital Signal
Solution:
  Amplitude:
  Period (T):
  Frequency (ƒ):
2V
4V
2ms
4ms
Notes: Here is the solution. If you print handouts, do not print this page. (1 of 2)

## Slide 13: Example: Digital Signal
Solution:
  Time High (tH):
  Time Low (tL):
  Duty Cycle (DC) %:
Notes: Here is the solution. If you print handouts, don’t print this page. (2 of 2)

## Slide 14: Period Measurement with Markers
The markers T1 and T2 can be used to measure the Period (T).
  Period (T) = 8ms
T1 = 8ms
T2 = 16ms
T2-T1 = 8ms

## Slide 15: Markers T1 and T2 can also be used to measure tH & tL
  Time High ( tH):
  Time Low ( tL):