## Slide 1
Asynchronous Counter
Digital Electronics

## Slide 2: Asynchronous Counters
This presentation will
Define asynchronous counters.
Define the terms states and modulus.
Provide multiple examples of asynchronous counters designed with D & J/K flip-flops.
Explain an asynchronous counter’s ripple effect.
Summarize the asynchronous counter design steps.

## Slide 3: Asynchronous Counters
Only the first flip-flop is clocked by an external clock. All subsequent flip-flops are clocked by the output of the preceding flip-flop.
Asynchronous counters are slower than synchronous counters (discussed later) because of the delay in the transmission of the pulses from flip-flop to flip-flop.
Asynchronous counters are also called ripple counters because of the way the clock pulses, or ripples, its way through the flip-flops.

## Slide 4: States / Modulus / Flip-Flops
The number of flip-flops determines the count limit or number of states:
States = 2 (# of flip-flops)
The number of states used is called the MODULUS.
For example, a Modulus-12 counter (Mod-12) would count from 0 (0000) to 11 (1011) and would require four flip-flops (24 = 16 states; 12 are used)

## Slide 5: Asynchronous Counter 1Bit: D Flip-Flop - Positive Edge Trigger
CLK
Q0
0
1
0
Repeats →

## Slide 6: Asynchronous Counter 2 Bit Up Counter: D Flip-Flops - Positive Edge Trigger
CLK
Q0
Q1
0
Repeats →
0
1
0
0
1
1
1
“0”
“1”
“2”
“3”
Since we want Q1 to toggle on the falling edge of Q0, we must clock the second flip-flop from the of the first.

## Slide 7: Asynchronous Counter 3 Bit Up Counter: D Flip-Flops - Positive Edge Trigger
CLK
Q0
Q1
Repeats →
0
0
0
1
0
0
0
1
0
1
1
0
0
0
1
1
0
1
0
1
1
1
1
1
Q2
“0”
“2”
“4”
“6”
“1”
“3”
“5”
“7”
The CLKs are connected to the of the previous flip-flop.

## Slide 8: The Ripple Effect
As the clock input “ripples” from the first flip-flop to the last, the propagation delays from the flip-flops accumulate. This causes the Q outputs to change at different times, resulting in the counter briefly producing incorrect counts. For example, as a 3 bit ripple counter counts from 7 to 0, it will briefly output the count 6 and 4.
CLK
Q0
Q1
Q2
1
1
1
0
0
0
1 mSec
100 nSec
7
1
1
1
4
1
0
0
6
1
1
0
0
0
0
0

## Slide 9: Asynchronous Counter 3 Bit Down Counter: D Flip-Flops - Positive Edge Trigger
CLK
Q0
Q1
Repeats →
1
1
1
0
1
1
1
0
1
0
0
1
1
1
0
0
1
0
1
0
0
0
0
0
Q2
“7”
“5”
“3”
“1”
“6”
“4”
“2”
“0”
Note: The CLKs are connected to the Q of the previous flip-flop.

## Slide 10: Asynchronous Counter Summary
Up Counters
  Connect the CLK input to the Q output with the opposite polarity.
Down Counters
  Connect the CLK input to the Q output with the same polarity.

## Slide 11: Asynchronous Counter 3 Bit Up Counter: JK Flip-Flops – Negative Edge Trigger
CLK
Q0
Q1
Repeats →
0
0
0
1
0
0
0
1
0
1
1
0
0
0
1
1
0
1
0
1
1
1
1
1
Q2
“0”
“2”
“4”
“6”
“1”
“3”
“5”
“7”
The active low CLKs are connected to the Q of the previous flip-flop.

## Slide 12: Asynchronous Counter 3 Bit Down Counter: JK Flip-Flops - Negative Edge Trigger
0
1
1
1
0
1
0
0
1
1
1
0
0
1
0
1
0
0
0
0
0
Q2
The active low CLKs are connected to the
of the previous flip-flop.
CLK
Q0
Q1
Repeats →
1
1
1
“7”
“5”
“3”
“1”
“6”
“4”
“2”
“0”

## Slide 13: Modulus Asynchronous Counter 3 Bit Mod-6 (0-5) Up Counter: D Flip-Flops
1
0
0
0
1
0
0
0
0
0
0
1
1
0
1
0
1
1
0
0
1
Q2
RESET
Q0
Q1
Repeats →
0
0
0
“0”
“2”
“4”
“0”
“1”
“3”
“5”
“1”
The upper limit of the count is 5; therefore, the reset circuit must detect a 6 (count +1).
Notes: The reset (clear) is low activation (a LOW triggers the CLEAR). If you watch carefully, you should see the number 110 display for just a fraction of a second before the NAND resets the count. You can also see the NAND gate flash low for a fraction of a second.
You may wish to lower the frequency even further to see this (5 Hz)

## Slide 14: Asynchronous Counter Design Steps
Select Counter Type
    Up or Down
    Modulus
Select Flip-Flop Type
    D (74LS74)
    J/K (74LS76)
Determine Number of Flip-Flops
    2 # Flip-Flops  Modulus
Design Count Limit Logic
    Input to reset logic circuit is count limit plus one for up counters (minus one for down counters)